## Slide 1: Deriving discharge using USGS stage
Supervisor: Dr. Bong Chul Seo
Presenter: Sujan Maharjan

## Slide 2: Study area

## Slide 3: Shift
Correction applied to stage-discharge relation, or rating, to compensate for variation in the rating
Shifts are temporary
Every Gage has their own shift, which are added to the gage heights
Caused due to man-made or natural changes in the river geometry

## Slide 4: Parameters tree
USGS Gage height at Thebes (GHT)
Shifted gage height
(GsH)
Shift (s)
Rating Table
Measured Fall (Fm)
Discharge Factor (Fm/Fr)
USGS Gage height at Cape Girardeau (GHC)
Datum of Gage +299.70 ft
Datum of Gage +304.27 ft
Difference
Rated Fall (Fr)
Sum
Product
Calculated USGS Discharge (QM)
Rated Discharge (QR)
When backwater effect is minimum to none

## Slide 5: Station of interest: Thebes
Has a high backwater effect
Uses slope rating method using the Gage height at the Cape Girardeau

## Slide 6: Data available
Rating curve from 2017-02-21
Rating curve dated 2025-06-18
Shift at Thebes in 30-minute interval
Gage height at Cape Girardeau and Thebes

## Slide 7: Methods
3 different types of extended rating table have been used to obtain the USGS discharge using the USGS stages
  [METHOD 1]: Using 2017-02-21 extended rating table
  [METHOD 2]: Using 2025-06-18 rating table from USGS website including the given shift
  [METHOD 3]: Using 2025-06-18 rating table from USGS website not including the given shift
  *It is brought to attention that the shift will be applied to gages in all methods. The shift being applied in Method 2 is to the rating curve in addition to the gages.

## Slide 8: Method 1
  [METHOD 1]: Using
  2017-02-21 extended rating table

## Slide 9: Method 2
  [METHOD 2]: Using
  2025-06-18 rating table from USGS website including shift
INDEP (ft) | SHIFT (ft) | Discharge (CFS) | Shifted Depth (ft)
1.81 | 0.19 | 54500.00 | 1.62
1.82 | 0.19 | 54554.97 | 1.63
1.83 | 0.19 | 54609.99 | 1.64
1.84 | 0.19 | 54665.04 | 1.65
1.85 | 0.19 | 54720.13 | 1.66
1.86 | 0.19 | 54775.27 | 1.67
1.87 | 0.19 | 54830.44 | 1.68
1.88 | 0.19 | 54885.66 | 1.69
1.89 | 0.19 | 54940.92 | 1.7
1.9 | 0.19 | 54996.22 | 1.71
1.91 | 0.19 | 55051.55 | 1.72
1.92 | 0.19 | 55106.93 | 1.73
1.93 | 0.19 | 55162.35 | 1.74
1.94 | 0.19 | 55217.81 | 1.75
1.95 | 0.19 | 55273.32 | 1.76
1.96 | 0.19 | 55328.86 | 1.77
1.97 | 0.19 | 55384.44 | 1.78
1.98 | 0.19 | 55440.07 | 1.79

## Slide 10: Method 3
  [METHOD 3]: Using 2025-06-18
  rating table from USGS website not including shift
INDEP (ft) | SHIFT (ft) | Discharge (CFS)
1.81 | 0.19 | 54500.00
1.82 | 0.19 | 54554.97
1.83 | 0.19 | 54609.99
1.84 | 0.19 | 54665.04
1.85 | 0.19 | 54720.13
1.86 | 0.19 | 54775.27
1.87 | 0.19 | 54830.44
1.88 | 0.19 | 54885.66
1.89 | 0.19 | 54940.92
1.9 | 0.19 | 54996.22
1.91 | 0.19 | 55051.55
1.92 | 0.19 | 55106.93
1.93 | 0.19 | 55162.35
1.94 | 0.19 | 55217.81
1.95 | 0.19 | 55273.32
1.96 | 0.19 | 55328.86
1.97 | 0.19 | 55384.44
1.98 | 0.19 | 55440.07

## Slide 11: Results
SN | Method | Mean average percentage error (%) | Normalized Root Mean Squared Error | Kling-Gupta Efficiency
1 | Method 1 | 0.69 | 0.312 | 0.9937
2 | Method 2 | 1.98 | 0.593 | 0.9812
3 | Method 3 | 0.79 | 0.277 | 0.9934

## Slide 12: Method 1 Results

## Slide 13: Method 2 Results

## Slide 14: Method 3 Results

## Slide 15: Queries
Which rating curve is the base rating curve for the given shifts (2017/2025)?
After a rating curve has been shifted and USGS publishes the new rating curve, does the shift apply to the new rating curve or still to the previous one?