## Slide 1: Deriving discharge using USGS stage
Supervisor: Dr. Bong Chul Seo
Presenter: Sujan Maharjan

## Slide 2: Study area

## Slide 3: Parameters tree
USGS Gage height at Thebes (GHT)
Shifted gage height
(GsH)
Shift (s)
Rating Table
Measured Fall (Fm)
Discharge Factor
USGS Gage height at Cape Girardeau (GHC)
+299.70 ft
+304.27 ft
Difference
Rated Fall (Fr)
Sum
Product
Calculated USGS Discharge
Rated Discharge
When backwater effect is minimum to none

## Slide 4: Station of interest: Thebes
Has a high backwater effect
Uses slope rating method using the Gage height at the Cape Girardeau
Chart: Rating curve at Mississipi river in Thebes
Chart: Rating curve at Mississippi river at Chester

## Slide 5: Data available
Rating curve from 2017-02-21
Rating curve dated 2025-06-18
Shift at Thebes in 30-minute interval
Gage height at Cape Girardeau and Thebes
Chart: USGS Shift Timeseries

## Slide 6: Methods
3 different types of extended rating table have been used to obtain the USGS discharge using the USGS stages
  [METHOD 1]: Using 2017-02-21 extended rating table
  [METHOD 2]: Using 2025-06-18 rating table from USGS website including the given shift
  [METHOD 3]: Using 2025-06-18 rating table from USGS website not including the given shift
  *It is brought to attention that the shift will be applied to gages in all methods. The shift being applied in Method 2 is to the rating curve in addition to the gages.

## Slide 7: Method 1
  [METHOD 1]: Using
  2017-02-21 extended rating table

## Slide 8: Method 2
  [METHOD 2]: Using
  2025-06-18 rating table from USGS website including shift
INDEP (ft) | SHIFT (ft) | Discharge (CFS) | Shifted Depth (ft)
1.81 | 0.19 | 54500 | 1.62
1.82 | 0.19 | 54554.97 | 1.63
1.83 | 0.19 | 54609.99 | 1.64
1.84 | 0.19 | 54665.04 | 1.65
1.85 | 0.19 | 54720.13 | 1.66
1.86 | 0.19 | 54775.27 | 1.67
1.87 | 0.19 | 54830.44 | 1.68
1.88 | 0.19 | 54885.66 | 1.69
1.89 | 0.19 | 54940.92 | 1.7
1.9 | 0.19 | 54996.22 | 1.71
1.91 | 0.19 | 55051.55 | 1.72
1.92 | 0.19 | 55106.93 | 1.73
1.93 | 0.19 | 55162.35 | 1.74
1.94 | 0.19 | 55217.81 | 1.75
1.95 | 0.19 | 55273.32 | 1.76
1.96 | 0.19 | 55328.86 | 1.77
1.97 | 0.19 | 55384.44 | 1.78
1.98 | 0.19 | 55440.07 | 1.79

## Slide 9: Method 3
  [METHOD 3]: Using 2025-06-18
  rating table from USGS website not including shift
INDEP (ft) | SHIFT (ft) | Discharge (CFS)
1.81 | 0.19 | 54500
1.82 | 0.19 | 54554.97
1.83 | 0.19 | 54609.99
1.84 | 0.19 | 54665.04
1.85 | 0.19 | 54720.13
1.86 | 0.19 | 54775.27
1.87 | 0.19 | 54830.44
1.88 | 0.19 | 54885.66
1.89 | 0.19 | 54940.92
1.9 | 0.19 | 54996.22
1.91 | 0.19 | 55051.55
1.92 | 0.19 | 55106.93
1.93 | 0.19 | 55162.35
1.94 | 0.19 | 55217.81
1.95 | 0.19 | 55273.32
1.96 | 0.19 | 55328.86
1.97 | 0.19 | 55384.44
1.98 | 0.19 | 55440.07

## Slide 10: Results
SN | Method | Mean average percentage error (%) | Normalized Root Mean Squared Error | Kling-Gupta Efficiency
1 | Method 1 | 0.69 | 0.312 | 0.9937
2 | Method 2 | 1.98 | 0.593 | 0.9812
3 | Method 3 | 0.79 | 0.277 | 0.9934

## Slide 11: Method 1 Results

## Slide 12: Method 2 Results

## Slide 13: Method 3 Results

## Slide 14: Queries
Which rating curve is the base rating curve for the given shifts (2017/2025)?
After a rating curve has been shifted and USGS publishes the new rating curve, does the shift apply to the new rating curve or still to the previous one?